## Slide 1: Digital Electronics
Art 317
Parker

## Slide 2: Digital VS Analog
Normal electronic circuits are analog, which means that things are continuous. Between any two voltages there is another voltage. Lights can be varying degrees of brightness, and sounds have many (infinite) levels of volume.

## Slide 3: Digital
Digital electronics is based one there being only TWO voltages. We presume that nothing else exists.
Also, digital electronics is often about time. One thing happens, then another, and another, triggered by a clock of by each other.

## Slide 4: Digital
When using digital electronics, we use little black boxes that have specific characteristics. Indeed, each little black box contains a complex electronics circuit.
But we don’t care. We only care about inputs and outputs.

## Slide 5: Digital
Here are the black boxes. Opamps are a black box too, but are not digital.

## Slide 7: Each chip has its own function, and low level ones have 1 or more ‘gates’ each of which does a particular LOGIC task.
What do digital chips do?
Logic involves TRUE and FALSE values that are each represented by a voltage.
Thus, a chip needs power supplied to it. The pin marked Vcc is +ve supply and GND is negative.

## Slide 8: Quad NAND gate
Note there are 4 gates on this chip.

## Slide 9
Each type of gate presents a true or false output that is a function of the true/false inputs.
Let’s use a numeric coding of true and false.
Let true = 1 and false = 0.

## Slide 10: The AND function
The result of AND is TRUE only when both inputs are TRUE.
0 AND 0 is 0
0 AND 1 is 0
1 AND 0 is 0
1 AND 1 is 1

## Slide 11: The AND function
Inputs are given names, but for this kind of gate the names are interchangeable
A B Output
0 0 0
0 1 0
1 0 0
1 1 1
Output
A
B

## Slide 12: Logic Circuits
TRUE ( or 1 or HI) is a voltage between 2 and 5
FALSE (or 0 or LOW) is between 0 and 0.8 volts
5 V
0 V
0 V
5 V
5 V
5 V

## Slide 13: Combinational Logic
These circuits are combined to make more complex ones.
So long as a clock is not needed to encode the values in the circuit, this is called combinational logic.

## Slide 14: Combinational Logic
A B C D Out
0 0 0 0 0
0 1 0 0 0
1 0 0 0 0
1 0 0 1 0
0 0 1 0 0
0 1 1 0 0
1 0 1 0 0
1 1 1 1 1
A
B
C
Out
D

## Slide 15: Combinational Logic
A B C Out
0 0 0 0
0 1 0 0
1 0 0 0
1 0 0 0
0 0 1 0
0 1 1 0
1 0 1 0
1 1 1 1
A
B
C
Out
The output is true only when all inputs are true. The output is “A and B and C”, or a 3 input AND gate.

## Slide 16: NOT
A NOT gate inverts the input.
If the input is TRUE, output is FALSE;
input is false, output is true.
NOT A can be written ~A or A
A
B
A B
0 1
1 0

## Slide 17: NOT
The invert circuit is just a small transistor circuit.
All gates are.

## Slide 18: NOT
The little circle at the right of the symbol is the one that really means ‘not’. So the original gate that we saw was an AND with a little circle, which means NOT AND, abbreviated to NAND

## Slide 19: NAND
AND NOT
A B Output
0 0 0 1
0 1 0 1
1 0 0 1
1 1 1 0

## Slide 20: NAND
NAND
A B Output
0 0 1
0 1 1
1 0 1
1 1 0

## Slide 21: NAND and Inverter
Connect the inputs to a NAND together. You get an inverter.
AND NOT
A Output
0 0 1
1 1 0
A

## Slide 22: Build a Circuit
Test an AND gate (or a NAND, etc.)

## Slide 23: Answer – pull-down resistors

## Slide 24: Other common gates: OR
A B Output
0 0 0
0 1 1
0 1
1 1 1

## Slide 25: Other common gates: NOR
A B Output
0 0 1
0 1 0
0 1 0
0 1 0

## Slide 26: Common Gates: Exclusive OR
Output is 0 when the inputs are equal.

## Slide 27: A functional Logic Circuit: ½ Adder
A and B are two inputs, 0 or 1. The half-adder returns the sum of the two and a carry.
0 + 0 = 0 with a carry of 0
0 + 1 = 1 with a carry of 0
1 + 0 = 1 with a carry of 0
1 + 1 = 0 with a carry of 1
Note that the sum part is an exclusive OR
The carry part is an AND.

## Slide 28: Half adder
So:

## Slide 29: Adders
This is the sum of a binary digit.
Shall I explain Binary numbers?

## Slide 30: Resuming an adder:
An adder will consist of a set of half-adders.
Two half-adders = 1 adder.
Each bit needs 1 adder.
1 0 1 0 0 + 20 +
0 1 1 0 1 13
We need 5 adders here.
Sum is 33

## Slide 31: Adders
Add A and B and a carry from a previous step. A and B are summed, and the output sum is added to the carry in. A carry out from either stage (OR) is the carry out from this adder.

## Slide 32: adding
1 0 1 0 0
0 1 1 0 1
0
0
0
1
1
0 0 0 0 1
1

## Slide 33: Adder
Sum is 33. Correct.